## Slide 1: Modernizing Network Infrastructure – Intel 10GbE Connectivity
15 January 2016

## Slide 2: Demand for 10GbE is Expected to Explode
Estimated Ethernet Port Growth through 2016
Notes: 10GbE has been around since about 2008. Adoption has been slow for two primary reasons:
The network was not the primary bottleneck in system performance
The relatively high cost of upgrading network infrastructure for 10GbE
With technology advances in processors, much faster flash storage combined with the increased use of virtualized servers, administrators are now looking to upgrade their network infrastructure. The following chart (credit Crehan Research, LRF 2015) illustrates the dramatic growth in the number of 10GbE ports expected in the next few years along with a corresponding drop in the number of 1GbE ports.

## Slide 3: Ethernet Adapter OEM Market Segment Breakdown
Credit: Crehn Research - Q3’15 Overall Ethernet LOM & NIC Port Market Segment Share
Leverage the Leader in NIC Adapter Sales
High volumes prove Intel’s high quality, support and customer satisfaction
Volume deployment and real-life user stressing of the products quickly eliminates any unknown issues
Deeper expertise and experience
Notes: Who is providing solutions into the 10GbE market? According to Crehan Research, Intel placed a commanding 7,425 ports shipped into the market in 2015 Q3, followed by Broadcom at 2,779 ports, QLogic at 484.7 ports and Emulex at 291 ports. The following chart shows the overall market segment share (MSS) for Ethernet LOM & NIC Ports.
Leveraging the leader in 10GbE NIC adapters

## Slide 4: Driving forces for 10GbE Adoption
Provide greater bandwidth for virtualized servers
Reduce complexities associated with using 1GbE for virtualized servers
Increase flexibility by combining data and storage networks on one unified network
Eliminate networking bottlenecks caused by technological advances such as faster processors and flash storage
Notes: The Intel white paper 10GBBase-T for Broad 10 Gigabit Adoption in the Data Center provides valuable information on the driving forces for the adoption of 10GbE and the alternatives for delivering it to the data center including pros and cons of each method.
The driving forces listed include:
Provide greater bandwidth for virtualized servers.
Reduce complexities associated with using 1GbE for virtualized servers
Increase flexibility by combining data and storage networks on one unified network
Eliminate networking bottlenecks caused by technological advances such as faster processors and flash storage

## Slide 5: Study: Market Pulse:10GbE Adoption
Top challenges include inability of bandwidth to keep up with:
  Faster servers
  Increased data volume
  Virtual Machine (VM) sprawl
93% of respondents expect their organizations’ bandwidth to grow over the next twelve months by an average of 28%
80% of the respondents have deployed or plan to deploy 10GbE
Credit: IDG Research Services
Notes: Intel and HP® commissioned IDG Research Services to do a study Market Pulse: 10GbE Adoption with InfoWorld and NetworkWorld. This study provides insight into the motivations for moving to 10GB and benefits organizations have experienced or expect to experience from the upgrade.
Key findings from the study include:
The top challenges for data centers and private cloud networks are the inability of bandwidth to keep up with faster servers, the increases in data volume, and Virtual Machine (VM) sprawl. 93% of respondents expect their organizations’ bandwidth to grow over the next twelve months by an average of 28%.
80% of the respondents have deployed or plan to deploy 10GbE
Of the respondents who have deployed or plan to deploy 10GbE
  The biggest drivers for deployment are data center agility and virtualization/private cloud.
  Large organizations (1,000 or more employees) are significantly more likely to cite consolidation of multiple GbE connections to 10GbE, and deployments of applications that require more bandwidth as drivers for 10GbE deployment.
  77% say their organizations are already experiencing increase in application performance
  67% say their organizations have experienced a more simplified network structure from their 10GbE deployment.

## Slide 6: “Which of the following did or will drive deployment of 10GbE at your organization?”
IDG Research: Market Pulse: 10GbE Adoption
Notes: Boosting data center agility and virtualization and/or private cloud deployments were the top reasons cited.

## Slide 7: “Which of the following benefits has your organization already experienced as a result of 10GbE deployments?”
IDG Research: Market Pulse: 10GbE Adoption
Notes: Top benefits, increased application performance and simplification.

## Slide 8: 10GbE Technology Choices
Several options are available to deploy 10GbE
  Which interface is the best depends on the data center topology and budget
10GbE interface alternatives for the data center include:
  10GBASE-CX4
  10GBASE-SR (SFP+ Optical fiber)
  10GBASE-SFP+ Direct Attach Copper (DAC)
  10GBASE-T
Notes: Several technologies are available to deploy 10GbE. Each have their strengths and weaknesses.

## Slide 9: Primary Markets for 10GbE and Greater
Enterprise Data Centers:
  Transitioning from 1Gb to 10Gb to leverage technologies
  Evaluating network overlays such as VXLAN, NVGRE, and STT
Cloud Service Providers & Communication Service Providers:
  Deploying 10GbE SFP+ and 10GBASE-T for service cloud workloads
  Evaluating 100GbE server ports for network intensive workloads
  Deploying 10GbE & 40GbE with DPDK (Data Plane Development Kit)
  Deploying NFV (network-function virtualization) on standards based servers
Notes: The primary market for networking infrastructure greater than 1000GbE includes the following broad categories:
Enterprise Data Centers
Customers transitioning from 1Gb to 10Gb to leverage new processor and disk technologies
Customers evaluating network overlays such as Virtual eXtensible Local Area Networks (VXLAN), Network Virtualization using Generic Routing Encapsulation (NVGRE), and Stateless Transport Tunneling (STT)
Cloud Service Providers
Deploying 10GbE SFP+ and 10GBBASET-T to provide for the network traffic needed to service cloud workloads
Evaluating and investigating 100GbE server ports for network intensive workloads
Communication Service Providers
Deploying 10GbE & 40GbE with DPDK (Data Plane Development Kit)
Deploying NFV (network-function virtualization) on standards based servers
Developing applications to leverage Intel’s new switch technology code named Red Rock Canyon

## Slide 10: 10GbE Technology - 10GBASE-CX4
Advantages
  Reach up to 15 meters
  Low Cost
  Low Power
  Low Latency
Disadvantages
  Larger diameter, fairly rigid cables purchased in fixed lengths, making it difficult to use in high density data centers
  Adoption is relatively low
Notes: The Intel white paper 10GBBase-T for Broad 10 Gigabit Adoption in the Data Center provides valuable information on the driving forces for the adoption of 10GbE and the alternatives for delivering it to the data center including pros and cons of each method.

## Slide 11: 10GbE Technology - 10GBASE-SR (SFP+ Optical fiber)
Advantages
  Reach up to 300 meters
  Low Power
  Low Latency
Disadvantages
  Optical connections may not be cost-effective for broad deployment
  Fiber electronics can cost as much as four or five times their copper counterparts
Notes: The Intel white paper 10GBBase-T for Broad 10 Gigabit Adoption in the Data Center provides valuable information on the driving forces for the adoption of 10GbE and the alternatives for delivering it to the data center including pros and cons of each method.

## Slide 12: 10GbE Technology - 10GBASE-SFP+ Direct Attach Copper (DAC)
Advantages
  Reach up to 7 meters
  Lower cost alternative to fiber
Disadvantages
  Not backward-compatible with existing GbE switches
  Cables are more expensive than structured copper channels, and cannot be field terminated
Notes: The Intel white paper 10GBBase-T for Broad 10 Gigabit Adoption in the Data Center provides valuable information on the driving forces for the adoption of 10GbE and the alternatives for delivering it to the data center including pros and cons of each method.

## Slide 13: 10GbE Technology - 10GBASE-T
Advantages
  Reach up to 100 meters
  Backward compatible with 1000BASE-T switch infrastructures using CAT6,CAT6A or above cabling
  Lowest cost media
  Operates in data center/low power mode if under 30 meters
  Process improvements from 25 Watts/port to under 6 Watt/port
Disadvantages
  Adds an incremental 2 µs of latency over 1000BASE-T
Notes: The Intel white paper 10GBBase-T for Broad 10 Gigabit Adoption in the Data Center provides valuable information on the driving forces for the adoption of 10GbE and the alternatives for delivering it to the data center including pros and cons of each method.

## Slide 14: Data Center Network Architectures Reference
Network Architecture | Technology | Connectivity
Top of Rack (ToR) | 10GBASE-SR (SFP+ Fiber) | Uplinks from ToR switches to aggregation layer switches
 | 10GBASE-SPF+ DAC | Inter-cabinet connectivity to switches
 | 10GBASE-CX4 | Inter-cabinet connectivity to switches
 | 10GBASE-T | Inter-cabinet connectivity to switches
Middle of Row (MoR) | 10GBASE-SR (SFP+ Fiber) | Inter-cabinet connectivity to switches
 | 10GBASE-T | Inter-cabinet connectivity to switches
End of Row (EoR) | 10GBASE-SR (SFP+ Fiber) | Inter-cabinet connectivity to switches
 | 10GBASE-T | Inter-cabinet connectivity to switches
Network Backbone | 10GBASE-SR (SFP+ Fiber) | Network data center connectivity
Notes: This reference provides information a cross-reference of appropriate technology based upon network architecture

## Slide 15: Intel 10GbE Solutions
#1 in the Market for 1GbE and 10GbE ports shipped
Intel - Works Better Together – Intel’s CPUs, when paired with Intel NIC controllers, provide performance benefits only Intel can deliver
Intel leverages innovative complementary technologies, like Intel VT, where the Intel CPU and Intel NIC share networking workloads and tasks – providing unmatched synergy
Notes: According to Crehan Research, Intel placed a commanding 7,425 ports shipped into the market in 2015 Q3, followed by Broadcom at 2,779 ports, QLogic at 484.7 ports and Emulex at 291 ports. The following chart shows the overall market segment share (MSS) for Ethernet LOM & NIC Ports.
Intel has integrated technology in both their processors and NIC cards to work together to provide performance benefits.

## Slide 16: Intel Complementary Technology Increases Performance
Intel Virtualization Technology (Intel VT)
Portfolio of technologies and features that add performance and functionality to virtualized environments by providing hardware assist to virtualization software
  CPU Virtualization
  Enables abstraction of Intel CPU power to a VM
  Memory Virtualization
  Allows abstraction, isolation, and monitoring of memory per VM Features include direct memory access (DMA) remapping, and extended page tables (EPT)
  I/O Virtualization
  Facilitates offloading the multi-core packet process to the network adapters. Allows direct assignment of VMs to virtual functions, including disk I/O
Notes: When upgrading a data center, each component upgraded to newer technology carries an increase in performance and functionality. In addition, when complementary Intel upgrades are selected, Intel provides technology that works across components to provide additional performance and functionality.
Intel Virtualization Technology (Intel VT) provides a portfolio of technologies and features that provide performance and functionality to increase the performance of systems running a virtualized environment by providing a hardware assist to the virtualization software. These technologies work to reduce the virtualization overheads occurring in cache, I/O, and memory in hypervisors for hypervisors, solution developers, and users who have enabled Intel VT. The result is a server’s virtual machines (VM) run more cost effectively. The Intel VT portfolio includes:
CPU virtualization features enable abstraction of the full power of the Intel CPU to a VM. Software in the VM can run as if it was running natively on a dedicated CPU. This feature also provides for live migration from one Intel CPU generation to another, as well as nested virtualization.
Memory virtualization features allow abstraction, isolation, and monitoring of memory on a per VM basis. These features facilitate live migration of VMs, add to fault tolerance, and enhance security. Features include direct memory access (DMA) remapping, and extended page tables (EPT), including their extensions: accessed and dirty bits, and fast switching of EPT contexts.
I/O virtualization features facilitate offloading the multi-core packet process to network adapters as well as direct assignment of virtual machines to virtual functions, including disk I/O.

## Slide 17: Intel VT feature: Virtual Machine Device Queues (VMDQ)
Improves traffic management within the server by offloading traffic sorting and routing from the hypervisor’s virtual switch to the Intel Ethernet Controller
Works with VMware NetQueue or Microsoft Virtual Machine (VM) Queues
Enables traffic steering and balanced bandwidth allocation across the Intel Ethernet Controller’s multiple hardware queues
Notes: Virtual Machine Device Queues (VMDQ) – Improves traffic management within the server by offloading traffic sorting and routing from the hypervisor’s virtual switch to the Intel Ethernet Controller. By working with VMware NetQueue or Microsoft Virtual Machine (VM) Queues, VMDQ enables traffic steering and balanced bandwidth allocation across the Intel Ethernet Controller’s multiple hardware queues.

## Slide 18: Intel VT feature: Single Root I/O Virtualization (SR-IVO)
Allows partitioning of a single Intel Ethernet Server Adapter port into multiple virtual functions
Virtual ports can be used to create multiple isolated connections to virtual machines
Can also be used to remove the CPU from the process of moving data to and from a VM
Data can be DMA’d directly to and from a VM without the software switch in the VM ever ‘touching’ it
Notes: Single Root I/O Virtualization (SR-IVO) – Allows partitioning of a single Intel Ethernet Server Adapter port into multiple virtual functions. Administrators can use these virtual ports to create multiple isolated connections to virtual machines. It can also be used to remove the CPU from the process of moving data to and from a VM. Data is DMA’d directly to and from a VM without the software switch in the VM ever ‘touching’ it.

## Slide 19: Intel VT feature: Intel Data Direct I/O (Intel DDIO)
Allows Intel Ethernet Controllers and adapters to talk directly with the processor cache
Intel DDIO makes the processor cache the primary destination and source of I/O rather than main memory
This re-architecture of the flow of I/O data, helps to deliver increased bandwidth, lower latency, and reduced power consumption
First introduced in the Intel Xeon processor E5 family and Intel Xeon processor E7 v2 family as a key feature of Intel Integrated I/O
Notes: Intel Data Direct I/O Technology enhancements (Intel DDIO) – First introduced in the Intel Xeon processor E5 family and Intel Xeon processor E7 v2 family as a key feature of Intel Integrated I/O. It allows Intel Ethernet Controllers and adapters to talk directly with the processor cache, Intel DDIO makes the processor cache the primary destination and source of I/O rather than main memory. This re-architecture of the flow of I/O data, helping to deliver increased bandwidth, lower latency, and reduced power consumption.

## Slide 20: Principled Technologies Study: Evaluating Impact of Component Upgrades
The study found that upgrading:
  CPU to the Intel Xeon processor E5-2699
  Operating system to Microsoft Windows Server 2012 R2
Produced a 16% increase in the number of VMs the system supported
Additional upgrades of:
  Standard SAS disk drives to Intel SSD DCS3700 drives
  Standard 1GbE to 10GbE Intel Ethernet CNA X520
Produced a 67% increase in the number of VMs system the supported
Notes: Intel commissioned Principled Technologies to evaluate the impact of upgrading processor, disk, and networking components both individually and together. In this study, the Principled Technologies labs found that by just upgrading to the CPU to the Intel Xeon processor E5-2699, and operating system to Microsoft Windows Server 2012 R2, resulted in a 16 % increase in the number of VMs the system could support. Additional upgrades from SAS disk drives to Intel SSD DCS3700 drives and 1GbE to 10GbE Intel Ethernet CNA X520 provided a 67% increase in the number of VMs supported.

## Slide 21: Principled Technologies Study- 67% Increase in VMs
Chart: Number of Virtual Machines Supported
| Base Configuation | Upgraded CPU & Operating System | Upgraded CPU, Operating System, Intel SSDs, Intel 10GbE
Series 1 | 24 | 28 | 40
Notes: This chart represents the results of the Principled Technologies study

## Slide 22: Intel Ethernet CNA X520
Features
Low cost, low power 10GbE performance
Provides 64 Virtual Station Interfaces
Flexible I/O virtualization for port partitioning
Compatible with Intel I/O Technology including VMDq, Next-Generation VMDq
Delivers same throughput as ten dual-port one gigabit adapters
Unified networking, delivering LAN, iSCSI and FCoE in one low cost CNA
Notes: Intel Ethernet Converged Network Adapter (CNA) X520 using Intel 82599 Controller
Benefits
Designed as a low cost, low power adapter, provides 10Gb Ethernet Blade, Direct Attach, or Fiber Optic Connectivity. Also provides a high-volume stable architecture with broad operating system support. Available as CNAs, LOM, and custom mezzanine adapters from most OEMs.
Features
Low cost, low power 10 Gigabit Ethernet (10GbE) performance
Provides 2 ports with 16 queues per port
Backward compatible with existing 1000BASE-T networks
Provides 64 Virtual Station Interfaces
Intel Ethernet Flow Director – TCP/IP or SCTP/IP protocols only
Compatible with Intel I/O Technology including VMDq, Next-Generation VMDq (64 queues per port)
Compatible with IPv6 Offloading, Advanced packet filtering
VLAN support with VLAN tag insertion, stripping and packet filtering for up to 4096 tags
Delivers same throughput as ten dual-port one-Gigabit adapters
Unified networking, delivering LAN, iSCSI and FCoE in one low cost CNA
Target Market
Enterprise networking — Customers needing networking performance, energy efficiency, broad Operating System (OS) and Virtual Machine Monitor (VMM) support, automation (including resource provisioning and monitoring, and workload balancing), converged networking, and emerging standards.

## Slide 23: Intel Ethernet CNA X540
Features
Low cost, low power 10GbE performance
Backward compatible with 1000BASE-T networks simplifies transition
Uses standard CAT-6A cabling with RJ45 connections
Provides 64 Virtual Station Interfaces
Flexible I/O virtualization for port partitioning
Unified networking, delivering LAN, iSCSI and FCoE in one low cost CNA
Industry First Dual-Port 10GBASE-T adapter with single-chip and integrated MAC + PHY
Notes: Intel Ethernet CNA X540 using Intel Ethernet Controller X540
Benefits
Brings 10 Gigabit 10BASE-T Ethernet to a broad market with reduced power, performance improvements, and deployment flexibility. Simplifies the transition to 10GbE through Backward Compatibility with existing 1GBE networks. Industry First Dual-Port 10GBASE-T adapter with single-chip solution with integrated MAC + PHY
Features
Low cost, low power 10 Gigabit Ethernet (10GbE) performance
Backward compatible with existing 1000BASE-T networks simplifies transition to 10GbE
Uses standard CAT-6a cabling with RJ45 connections
Flexible I/O virtualization for port partitioning and quality of service (QoS) of up to 64 virtual ports
Unified networking, delivering LAN, iSCSI and FCoE in one low cost CNA
Target Market
Enterprise networking — Customers needing 10BASE-T networking performance, energy efficiency, broad Operating System (OS) and Virtual Machine Monitor (VMM) support, automation (including resource provisioning and monitoring, and workload balancing), converged networking, and emerging standards.

## Slide 24: Intel Ethernet CNA XL710 & CNA X710
Features
Low power single chip design for PCI Express 3.0
Software configurable Ethernet Port Speed for up to 2x10GbE or up to 2x20GbE
Interfaces for Converged Network Adapters (CNA), backplanes and LAN on Motherboard
Provides 384 Virtual Station Interfaces
Intelligent load balancing for high performance traffic flows of virtual machines
Intelligent Offloads deliver high performance for NAS (NFS, SMB), and SAN (iSCSI)
Intel Ethernet Flow Director for hardware based application traffic steering
Intel Data Direct I/O (Intel DDIO) makes the processor cache the primary destination and source of I/O data rather than main memory
Notes: Intel Ethernet CNA XL710 and Ethernet CNA X710
Benefits
Brings 10 Gigabit Ethernet to the broad market with reduced power, performance improvements, and deployment flexibility. The XL710 can be deployed as Converged Network Adapters (CNA), backplanes, and LAN on Motherboard (LOM).
Features
Low power single chip design for PCI Express 3.0
Software configurable Ethernet Port Speed for up to 2x10GbE or up to 2x20GbE
Interfaces for Converged Network Adapters, backplanes and LAN on Motherboard
Network virtualization Overlay stateless offloads for Geneve, VXLAN, and NVGRE
Intelligent load balancing for high performance traffic flows of virtual machines
Intelligent Offloads accelerate operating system storage initiators to deliver high performance for NAS (NFS, SMB), and SAN (iSCSI)
Intel Data Plane Development Kit (DPDK) optimized for efficient packet processing to support Network Function Virtualization (NFV)
Intel Ethernet Flow Director for hardware based application traffic steering
Intel Data Direct I/O (Intel DDIO) makes the processor cache the primary destination and source of I/O data rather than main memory
Target Market
Enterprise networking — Customers needing networking performance, energy efficiency, broad Operating System (OS) and Virtual Machine Monitor (VMM) support, automation (including resource provisioning and monitoring, and workload balancing), converged networking, and emerging standards. Examples are data centers looking for Data Center Bridging (DCB) and Virtual Bridging (VEB).
Cloud networking — Cloud customers needing computing infrastructure and software are sold as services, and where cloud service providers drive unique requirements, the XL710 has these strengths: networking performance, energy efficiency, automation (including resource provisioning and monitoring, and workload balancing), sophisticated packet header parsing, and quality open source drivers. In the case where computing infrastructure is sold as a service, the XL710 features important in Enterprise networking and HPC can also be important to the cloud.

## Slide 25: Target Market for Intel Ethernet 40Gb/10Gb XL710/X710
Enterprise Networking Customers Needing:
  Networking performance
  Energy Efficiency
  Broad Operating System (OS) and Virtual Machine Monitor (VMM) support
  Automation (including resource provisioning and monitoring, and workload balancing)
  Converged networking, and emerging standards.
  Examples are data centers looking for Data Center Bridging (DCB) and Virtual Bridging (VEB).
Notes: The Intel XL710 and X710, due to their ability to provide 40GbE, have particular markets where increased network speed is an advantage.

## Slide 26: Target Market for Intel Ethernet 40/10Gb XL710/X710
Cloud Networking, Computing Infrastructure and Software as a Service (SaaS) Customers needing:
  Networking Performance
  Energy Efficiency
  Automation including resource provisioning and monitoring, and workload balancing
  Sophisticated packet header parsing, and quality open source drivers
Notes: The Intel XL710 and X710, due to their ability to provide 40GbE, have particular markets where increased network speed is an advantage.

## Slide 27: Intel 10GbE Comparison
Networking Specification | Intel Ethernet Controller XL710 and X710 | Intel Ethernet Controller X540 | Intel Ethernet Controller X520
Ports | 1x40GbE or 4x10GbE, Single/Dual | Single/Dual | Single/Dual
Data Rate Per Port | 40GbE/10GbE/1GbE | 10GbE/1GbE | 10GbE/1GbE
System Interface | PCIe v3.0 (8.0GT/s) | PCIe v2.1 (5.0 GT/s) | PCIe v2.0 (5.0GT/s)
Controller | FTXL710 | Intel X540 | Intel 82599ES
Interfaces including: SFI, KR, KR4, XAUI, KX, KX4, SGMII | Yes | No | No
Intel Ethernet Flow Director | Up to 64 different packet types including, TCP/IP, SCTP/IP,UDP,L2,IPV4, IPv6 | TCP/IP, SCTP/IP, Tx/Rx IP, UDP, IPv4, IPv6 | TCP/IP or SCTP/IP Only
Connectivity | Fiber-optic QFSP+: 40GBASE-SR4 or 40GBASE-LR4 or Copper Direct Attach or QFSP+CR4 | RJ45 Copper: 10GBASE-T,1000BASE-T, 100BASE-T | Fiber-optic SFP+: 10GBASE-SR or 10GBASE-LR or Copper Direct Attach
Notes: Features reference of Intel 10GbE solutions

## Slide 28: Intel 10GbE Comparison
Advanced Technologies |  |  | 
iWarp/RDMA | Yes | Yes | No
IEEE 1588 | Yes | No | No
Intel Ethernet Power Management | Yes | No | No
Intel Data Direct I/O Technology | Yes | Yes | Yes
Intelligent Offloads | Yes | Yes | Yes
Storage over Ethernet | iSCSI, NFS | iSCSI, NFS, FCoE | iSCSI, NFS, FCoE
Intel Virtualization Technology for Connectivity |  |  | 
Host Virtualization | 384 Virtual Station Interfaces | 64 Virtual Station Interfaces | 64 Virtual Station Interfaces
On-chip QoS and Traffic Management | Yes | Yes | Yes
Flexible Port Partitioning | Yes | Yes | Yes
Virtual Machine Device Queues (VMDq) | Yes | Yes | Yes
PCI-SIG SR-IVO Capable | Yes | Yes | Yes
Notes: Features reference of Intel 10GbE solutions

## Slide 29: Study: Market Pulse:10GbE Adoption
Key findings of those who have deployed or plan to deploy 10GbE
  The biggest drivers for deployment are data center agility and virtualization/private cloud deployments
  Large organizations (1,000+ employees) are significantly more likely to cite two factors as drivers for 10GbE deployment:
    Consolidation of multiple GbE connections to 10GbE
    Deployments of applications requiring more bandwidth
  77% say their organizations are already experiencing increase in application performance
  67% say their organizations have experienced a more simplified network structure
Credit: IDG Research Services
Notes: Intel and HP® commissioned IDG Research Services to do a study Market Pulse: 10GbE Adoption with InfoWorld and NetworkWorld. This study provides insight into the motivations for moving to 10GB and benefits organizations have experienced or expect to experience from the upgrade.
Key findings from the study include:
Of the respondents who have deployed or plan to deploy 10GbE
  The biggest drivers for deployment are data center agility and virtualization/private cloud.
  Large organizations (1,000 or more employees) are significantly more likely to cite consolidation of multiple GbE connections to 10GbE, and deployments of applications that require more bandwidth as drivers for 10GbE deployment.
  77% say their organizations are already experiencing increase in application performance
  67% say their organizations have experienced a more simplified network structure from their 10GbE deployment.

## Slide 30: Backup Slides

## Slide 31: HP Network Reference – Rack PCIe Adapters
HP Part # | 716591-B21 | 665249-B21 | 652497-B21 | I350T4V2 | 727055-B21
HP Description | HP 561-T2 Dual Port Adapter 10GBASE-T | HP 560SFP+ Dual Port Adapter SFP+ | HP 361T Dual Port Gigabit Server Adapter | HP 366T Quad Port Gigabit Server Adapter | HP 562 Dual Port Adapter SFP+
HP Platform | Gen 8, 9 | Gen 7, 8, 9 | Gen 7, 8, 9 | Gen 7, 8, 9 | Gen 9
Availability as of 12/15 | Yes | Yes | Yes | Yes | Coming Soon
Speed | 10GbE/1GbE | 10GbE | 1GbE | 1GbE | 10GbE
Ports, Media | Dual Port, 10BASE-T | Dual Port, SFP+ | Dual Port, 1000BASE-T | Quad Port, 1000BASE-T | Dual Port, SFP+
Form Factor | Server Adapter | Server Adapter | Server Adapter | Server Adapter | PCIe Server Adapter
Controller | Intel Ethernet Controller X540 | Intel Ethernet Controller X520 | Intel Ethernet Controller I350 | Intel Ethernet Controller I350 | Intel Ethernet Controller X710
Notes: Product numbers of Intel NIC adapters

## Slide 32: HP Network Reference – Blade Adapters
HP Part # | 615729-B21 | 665246-B21 | 655639-B21 | 727053-B21 | 727052-B21
HP Description | HP NC366M Quad Port Gigabit BL-c Adapter | HP 560M Dual Port 10 Gigabit BL-c Adapter | HP 560FLB Dual Port 10 Gigabit FlexLOM for BladeSystems | HP M600M Dual Port 20 Gigabit Mezzanine Adapter | HP 660FLB Dual Port 20 Gigabit FlexLOM for BladeSystems
HP Platform | Gen 7, 8, 9 | Gen 7, 8, 9 | Gen 8, 9 | Gen 9 | Gen 9
Availability as of 12/15 | Yes | Yes | Yes | Q1 2016 | Coming Soon
Speed | 1GbE | 10GbE/1GbE | 10GbE/1GbE | 20GbE | 20GbE
Ports, Media | Quad Port, KX | Dual Port, KR | Dual Port, KR | Dual Port, KR | Dual Port, KR
Form Factor | Mezzanine Card | Mezzanine Card | Flex-LOM Blade | Mezzanine Card | Flex-LOM Blade
Controller | Intel Ethernet Controller I350 | Intel Ethernet Controller X520 | Intel Ethernet Controller X520 | Intel Ethernet Controller XL710 | Intel Ethernet Controller XL710
Notes: Product numbers of Intel NIC adapters

## Slide 33: HP Network Reference – Rack FlexLOM Adapters
HP Part # | 665240-B21 | 665243-B21 | 716599-B21 | 700699-B21 | 727054-B21
HP Description | HP 366FLR Quad Port Gigabit Adapter | HP 560 FLR Dual Port Adapter SFP+ for Racks | HP P560 FLR Single Port Adapter SFP+ for Racks | HP 561FLR-T Dual Port Adapter 10GBASE-T | HP 562 FLR Dual Port Adapter SFP+ for Racks
HP Platform | Gen 8, 9 | Gen 8, 9 | Gen 8, 9 | Gen 8, 9 | Gen 9
Availability as of 12/15 | Yes | Yes | Yes | Coming Soon | Yes
Speed | 1GbE | 10GbE | 10GbE/1GbE | 10GbE | 10GbE/1GbE
Ports, Media | Quad Port, 1000BASE-T | Dual Port, SFP+ | Single Port, SFP+ | Dual Port, 10BASE-T | Dual Port, SFP+
Form Factor | Flex-LOM R&T | Flex-LOM R&T | Flex-LOM R&T | Flex-LOM R&T | Flex-LOM R&T
Controller | Intel Ethernet Controller I350 | Intel Ethernet Controller X520 | Intel Ethernet Controller X520 | Intel Ethernet Controller X540 | Intel Ethernet Controller X710
Notes: Product numbers of Intel NIC adapters

## Slide 34: Lenovo Network Reference – Copper Rack and Tower Adapters
Lenovo Part # | SN30G46430 | Dual: 0B94241 Quad 00JY854 | 00JY855 | 00JY856 | Dual:SN30G99689 Quad:SN30G99691
Lenovo Description | Intel® Ethernet Server Adapter I210-T1 | Intel® Ethernet Server Adapter I350-T2/T4 | Intel® Ethernet CNA X520-DA2 SFP+ | Intel® Ethernet Server CNA X540-T2 | Intel® CNA XL710-DA2/DA4
LenovoPlatform | M3/M4/M5 | M3/M4/M5 | M3/M4/M5 | M3/M4/M5 | M3/M4/M5
Avail as of 12/15 | Yes | Yes | Yes | Yes | Coming Soon
Speed | 1GbE | 1GbE | 10GbE | 10GbE | 10GbE
Ports, Media | Single Port, 1000BASE-T | Dual Port, Quad Port, 1000BASE-T | Dual Port, SFP+ | Dual Port, 10GBASE-T | Dual Port, Quad Port, SFP+
Form Factor | Server Adapter | Server Adapter | Server Adapter | Server Adapter | Server Adapter
Controller | Intel® Ethernet Controller I210AT | Intel® Ethernet Controller I350 | Intel® Ethernet Controller X520 | Intel® Ethernet Controller X540 | Intel® Ethernet Controller XL710
Notes: Product numbers of Intel NIC adapters

## Slide 35: Lenovo Network Reference – Embedded Adapters/Flex-LOMs
Lenovo Part # | Single: SN30G99685 Dual: SN30G99687 | 00JY857 | Quad: SN30H04306 | 11015441 | 11015442
Lenovo Description | Intel® Ethernet Converged Network Adapter XL710-QDA1/QDA2 | Intel® ETH 10GSFP+ DP EMBD CNA X520-2 | Intel® Ethernet X710-DA4 mLOM | Lenovo Think Server X520-2 Any Fabric | Lenovo ThinkServer I350-T4 AnyFabric
Lenovo Platform | M3/M4/M5 | M4 | TBD | TBD | TBD
Availability as of 12/15 | Coming Soon | Yes | Coming Soon | Yes | Yes
Speed | 40GbE/10GbE | 10GbE | 10GbE | 10GbE | 1GbE
Ports, Media | Single Port, Dual Port, QSFP+ | Dual Port, SFP+ | Quad Port, SFP+ | Dual Port, SFP+ | Quad Port, 1000BASE-T
Form Factor | Standard Server Adapter | Embedded Adapter | Flex-LOM | Flex-LOM | Flex-LOM
Controller | Intel® Ethernet Controller XL710 | Intel® Ethernet Controller X520 | Intel® Ethernet Controller XL710 | Intel® Ethernet Controller X520 | Intel® Ethernet Controller I350
Notes: Product numbers of Intel NIC adapters

## Slide 36: Lenovo Network Reference – ML2 Adapters
Lenovo Part # | 11015440 | 00JY941 | System X: 00D1994 | System X: 00D1998 | 11015440
Lenovo Description | Lenovo ThinkServer X540-T2 AnyFabric | 4x10 (FVL) Coyote Flat DA2 | Intel X540 ML2 Dual Port 10GbaseT Adapter for Lenovo System x | I350-T4 ML2 Quad Port GbE Adapter for Lenovo System x | Lenovo ThinkServer X540-T2 AnyFabric
Lenovo Platform | TBD | M5 | M5 | M5 | TBD
Availability as of 12/15 | Yes | Yes | Yes | Yes | Yes
Speed | 10GbE | 10GbE | 10GbE | 1GbE | 10GbE
Ports, Media | Dual Port, 10GBASE-T | Quad Port, SFP+ | Dual Port, 10GBASE-T | Quad Port, 1000BASE-T | Dual Port, 10GBASE-T
Form Factor | Flex-LOM | ML2 Adapter | ML2 Adapter | ML2 Adapter | Flex-LOM
Controller | Intel® Ethernet Controller I350 | Intel® Ethernet Controller I350 | Intel® Ethernet Controller I350 | Intel® Ethernet Controller I350 | Intel® Ethernet Controller I350
Notes: Product numbers of Intel NIC adapters